Item (Granular display)	Qty.	Purpose	Reference
Arduino Mega (Atmega2560)	1	Microcontroller. / 54 I/Os for motor drivers and future expansion.	Link
MOSFETs	2	Drivers for pump motor and solenoid valve. / Minimum 1A, 12V.	Link
Solenoid valve	1	Valve for controlling air tube.

Item (XYZ stage)	Qty.	Purpose	Reference
Stepper drivers	3	Drivers for stepper motors on X, Y, Z axes.	Link
Limit switches	3	For homing X, Y, Z axes.	Link
Stepper motors	3	For moving X, Y, Z axes. / Use NEMA 17 for ease of design. / High torque not necessary.
Timing belts and Pulleys	2m, 2	For moving the XY platform.	Link
Threaded rod and Coupler	1, / 1	For moving the pin pressing against the grains. / Rod diameter = 8mm is a good starting point.

Additional items:
- Jumper wires, breadboard.
- 5V regulator.
- Diodes, resistors, capacitors.